## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26037
Problem Statement Title- Adaptive Path Planning and Collision Avoidance for Autonomous Vehicles on Unstructured Indian Roads
Theme- Smart Vehicles
PS Category- Software
Team ID- (To be filled by team on SIH portal)
Team Name- Tech Vision

## Slide 2: Adaptive Autonomous Navigation
Proposed Solution
Detailed explanation of the proposed solution
An AI-driven adaptive path-planning stack: sensor fusion (LiDAR + camera + radar) builds a drivable-space map instead of relying on lane markings; a hybrid Hybrid-A*/Reinforcement-Learning planner generates real-time trajectories; an MPC controller with a potential-field safety layer executes collision-free motion around potholes, mixed traffic and unmarked roads
How it addresses the problem
Replaces lane-based navigation (unreliable on Indian roads) with drivable-area segmentation and multi-agent trajectory prediction tuned to erratic mixed traffic - two-wheelers, pedestrians, animals and carts - enabling safe navigation without lane markings or predictable traffic behaviour
Innovation and uniqueness of the solution
India-specific trained perception models, dynamic risk-based collision buffers (vs. fixed lane buffers), a hybrid classical + learning planner balancing safety guarantees with adaptability, and a low-cost sensor suite viable for price-sensitive Indian deployment.
Tech vision

## Slide 3: TECHNICAL APPROACH
Technologies to be used:
Python, ROS2, PyTorch/OpenCV for perception and planning; Hybrid A* and Deep RL (PPO) for path planning; Kalman/particle filter sensor fusion; LiDAR, stereo camera, radar and GPS-IMU on an NVIDIA Jetson Orin edge compute unit; CARLA/LGSVL simulator for Indian-road scenario testing
Methodology and process for implementation:
Pipeline: Perception (drivable-area segmentation + obstacle detection) to Trajectory Prediction to Global Path (Hybrid A*) to Local Planner (RL-refined) to MPC Controller to Actuation, with an emergency-braking safety layer running in parallel; validated first in simulation, then on a low-speed prototype vehicle in a controlled campus environment
Tech vision

## Slide 4: FEASIBILITY AND VIABILITY
Analysis of the feasibility of the idea
  Modular, simulation-first architecture keeps early costs low; falling prices of solid-state LiDAR and edge-AI boards (e.g. Jetson Orin) make a phased rollout - simulation, then a low-speed campus prototype, then pilot deployment - practically achievable
Potential challenges and risks
  Unpredictable mixed-traffic and animal behaviour, inconsistent lane markings and road quality, GPS multipath in dense urban areas, limited real-time compute on edge hardware, scarcity of annotated Indian-road datasets, and regulatory/safety certification
Strategies for overcoming these challenges
  Curate an India-specific annotated dataset (crowdsourced + simulation-generated); use sensor-fusion redundancy (IMU + wheel + visual odometry) for GPS-denied zones; compress/quantise models for edge deployment; roll out in ADAS-assist mode before full autonomy; partner with local transport authorities for controlled pilot zones
Tech vision

## Slide 5: IMPACT AND BENEFITS
Potential impact on the target audience
  Safer autonomous mobility for Indian conditions - last-mile delivery robots, campus/industrial shuttles, ride-hailing in tier-2/3 cities, and agricultural and rural transport, where roads are largely unstructured
Benefits of the solution:
  Social: fewer road accidents and safer transport for the elderly and disabled, in a country with among the highest road-fatality counts worldwide. Economic: lower logistics costs and a domestic market for India-tuned AV components. Environmental: optimised routing cuts fuel use and idling, supporting EV shuttle deployment
Tech vision

## Slide 6: RESEARCH AND REFERENCES
Details / Links of the reference and research work
  India Driving Dataset (IDD) - IIIT Hyderabad and Intel Labs, an unstructured-environment driving dataset (WACV 2019)
  Dolgov et al., "Practical Search Techniques in Path Planning for Autonomous Driving" - Hybrid A* algorithm
  Fox, Burgard and Thrun, "The Dynamic Window Approach to Collision Avoidance" - IEEE RAM, 1997
  Dosovitskiy et al., "CARLA: An Open Urban Driving Simulator" - CoRL 2017
  Ministry of Road Transport and Highways (MoRTH), "Road Accidents in India" annual report
Tech vision